## Slide 1: Overview of the microalgae production process
Koenraad Muylaert

## Slide 2
Notes: We use biomass for a wide variety of plant species, but so far we almost exclusively use terrestrial plants. There Is also plants life in the oceans = microalgae, microscopic plants growing near the surface of our oceans and lakes. It’s important: about half of the biomass produced on this planet is produced by these microalgae. There is a wide diversity to choose from: they are a evolutionary old group, metabolic diversity is much higher than for land plants.

## Slide 3
Historical use of microalgae (Spirulina, Tsjaad)

## Slide 4: Photosynthesis
Conversion efficiency for solar to chemical energy:
Maximum efficiency of photosynthesis: 12%
  Belgium: 180 ton/ha/year
Short-term realised efficiency in experimental systems: 4%
  Belgium: 60 ton/ha/year
Long-term realised efficiency in commercial systems: 2%
  Belgium: 30 ton/ha/year

## Slide 5: Productivity of microalgae
Microalgae (lab)
Microalgae (practice)
35 ton
90 ton
25 ton
11 ton
Corn
Soy
29 ton
17 ton
Potato
Sugar beet
18 ton
Wheat
Best practice annual production in ton dry biomass (leaves, stems, fruits) per hectare per year

## Slide 7
Production of Arthrospira in open ponds in Hawaii

## Slide 8
Production of Chlorella in a ‘photobioreactor’ in Germany

## Slide 9: Cultivation of microalgae
Open systems (raceway ponds) Closed systems (photobioreactors)
Relatively cheap Expensive
Sensitive to contamination Resistant to contamination
Inefficient light use (respiration) Efficient light use
Low biomass concentration High biomass concentration
Experience in commercial systems Little experience on large scale

## Slide 10: Biomass composition of microalgae
fibre
lipids
sugars
protein
soybean
microalgae

## Slide 11: Biomass composition
NO3-, NH4+
CO2
proteins
proteins
sugars
lipids

## Slide 12
Growth under sufficient N supply
light
H2O
O2
NADPH
é
Photosynthetic light reactions
Photosynthetic dark reactions
glucose
ATP
Amino acid synthesis
NO3-
NH4+
glutamine
Calvin
PROTEINS
N supply and biomass composition
CO2

## Slide 13
Growth under N limitation
light
H2O
O2
NADPH
é
Photosynthetic light reactions
Photosynthetic dark reactions
glucose
ATP
Calvin
starch/glycogen
N supply and biomass composition
CO2

## Slide 14: Biomass composition
high N, low CO2
low N, high CO2
proteins
proteins
sugars
lipids

## Slide 15: Harvesting microalgae
Challenges:
small cells: 5-10 µm diameter
low biomass concentration:
0.5 g dry matter L-1
stable suspensions
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
Notes: Cell suspnesions stabilized by negative surface charge of microalgae

## Slide 16: Harvesting microalgae
Challenge: low biomass concentration due to self-shading of cells (0.5 g dry weight L-1)
assume 10 ha open pond facility with productivity of 350 ton year-1
standing crop biomass is only 10 ton
facility should process 2000-3000 m3 day-1 to harvest 350 ton

## Slide 17: Wet biomass
drying and storage or processing of wet biomass?

## Slide 18: Cell wall disruption
high pressure homogenisation
ultrasound
enzymatic process
…

## Slide 19
Notes: Current production of microalgae for high-value products: technologies are too expensive for fuel production.

## Slide 20: Energy balance
Energy output:
Energy content of biomass: 17.5 MJ/kg
Energy input:
Heat (drying of biomass): 13.7 MJ/kg
Electricity: 2.7 MJ/kg
Fertiliser: 3.4 MJ/kg
Infrastructure: 3.5 MJ/kg
Net energy balance: -5.8 MJ/kg
Lardon, L. et al. 2009 “Life-cycle assessment of biodiesel production from microalgae” Environmental Science & Technology 43: 6475-6481.

## Slide 21: Need to optimise the production process
Notes: Production process needs to be optimized, just as we did for conventional agriculture.

## Slide 22: Current production and markets of microalgae
Total production 10 000 ton/year, market value 1 billion $/year,
nutritional supplements, cosmetics, natural pigments (25 – 300 $/kg)

## Slide 23: Unique bioproducts
lipids/fatty acids
pigments
polysaccharides, sugars
0

## Slide 24
Natural pigments

## Slide 25: Processed products
phycocyanin: blue food colourant
astaxanthin: additive in salmon feed
emerging application: long-chain polyunsaturated fatty acids (EPA, DHA)

## Slide 26: Conclusion
high productivity + attractive biomass composition = promising new biomass feedstock
complex production process = high cost of biomass
cost reduction required in all steps of production process to become competitive with conventional biomass feedstocks
microalgae as source of chemicals:
  low cost / high volume building blocks: scale increase and cost reduction required
  specialty chemicals, additives: perhaps, but no silver bullet…

## Slide 27: ALPO: Sara Cuellar
Chart: 
| Controle | N tekort
Proteïne | 36.5 | 10.4
Suikers | 13.5 | 73.7
carbohydrate accumulation in Arthrospira induced by N stress: changes in metabolism (photosynthesis, metabolic pathways)
harvesting of Arthrospira by screening

## Slide 28: ALPO: An Verfaillie
use of cationic nanocellulose crystals for harvesting and cell disruption in Chlorella
preparation of nanocellulose crystals from waste biomass